## Slide 1: DC Power Supply
Under the supervision of Dr.Sherif Hekal
Eng.Sara Adel

## Slide 2
Our Team
Abdelrahman Salah el-dein Abdelaziz
Mohamed Ahmed Mohamed Hassan
Farida Waheed Abd El Bary
Raneem Ahmed Refaat

## Slide 3: AIM OF THE PROJECT
It is to construct an adjustable regulated power supply that can provide DC voltage ranging from 1.2-30V. As the electric circuit consists of an AC Transformer followed by a rectifier bridge then smoothing capacitor and an adjustable voltage regulator integrated circuit.

## Slide 4: PROJECT STAGES STEP 2 STEP 1 STEP 3
Put our circuit on one of the simulator programs which is proteus to check it.
Design the project by select the components and choose suitable values for them.
Then we start the practical process.

## Slide 5: TABLE OF COMPONENTS 04 05 06 01 02 03 Bridge Rectifier Adjustable Voltage Regulator Transformer Resistor Potentiometer Capacitor
It’s value and number used in the project: 18K,220 with 5% , 2 Resistors
It’s value and number used in the project: 5K , 1 Potentiometer
It’s value and number used in the project: 2200micro-farad , 0.1micro-farad , 1micro-farad , 40V , 3 Capacitors
It’s value and number used in the project: 100V-3A , 1 Bridge
It’s value and number used in the project: 1.2V-37V , 1 LM317
It’s value and number used in the project: 24V-3A , 1 Transformer

## Slide 6: Diode Switch Connectors Plug Wires Banana Plug Connectors TABLE OF COMPONENTS 07 08 09 10 11 12
Its type: 2 Wire plug & Cord
It’s color: Red and Black
It’s value and number used in the project: 400V,1A , 1 Diode
It’s type: ON/OFF Rocker Switch

## Slide 7: 15 16 13 14 LED Soldering Iron PCB Board Fuse TABLE OF COMPONENTS
It’s color: Red

## Slide 8: SMALL HINT ON EACH COMPONENT Bridge Rectifier Transformer Adjustable Voltage Regulator
It is a convertor that convert the Alternating Current (AC) to Direct Current (DC).
It is basically a voltage control device that’s used widely in the distribution and transmission of alternating current power.
It is a regulator that can output adjustable voltages from anywhere in the range that the voltage regulator is designed to output.

## Slide 9: Resistor Capacitor Potentiometer SMALL HINT ON EACH COMPONENT
A passive electrical component with two-terminals that are used for limiting the flow of electric current in electrical circuits.
It is passive electronic component and has the capacity to store energy in the form of an electrical charge.
A passive electrical component with three-terminal resistor with a rotating contact that forms an adjustable voltage divider.

## Slide 10: Diode Connector Switch SMALL HINT ON EACH COMPONENT
It is a semiconductor device that essentially acts as a one-way switch for current which allows current to flow easily in one direction.
A connector is a device that joins two pieces of equipment, wire, or piping together
A device that opens and closes an electric circuit.

## Slide 11: Plug Banana Plug Connector Wires SMALL HINT ON EACH COMPONENT
It connects electric equipment to the alternating current (AC) power supply in buildings and on other sites.
They are electrical connectors that are used to join single-conductor wires to each other or to pieces of equipment.
A power cord is an electrical component used for connecting appliances to an electrical utility or power supply.

## Slide 12: Soldering Iron PCB LED SMALL HINT ON EACH COMPONENT
It is a hand tool used in soldering. It supplies heat to melt solder so that it can flow into the joint between two workpieces.
It is a medium used in electrical and electronic engineering to connect electronic components to one another in a controlled manner.
It is a semiconductor device that emits light when current flows through it.

## Slide 13: THE DESIGN ON PCB
After we designed the circuit, and put it on the simulator program (proteus) it gave us voltage ranging from 1.25V to 29.9V.
So, we went on and printed our design on the PCB.

## Slide 14: THE DESIGN ON PROTEUS

## Slide 15: AFTER THAT We went on and buy our components. Then plugged it in the plug to a power source, opened the switch. Then we joined the components together on the PCB using soldering iron.
We checked the voltage using digital multimeter (AVO) it gave us a voltage ranging from 1.2V to 31.5 V.

## Slide 16: THANK YOU!